## Slide 1: #define hell in multi-platform embedded programming
Tore Martin Hagen
Software Architect Schlumberger
Notes: 4/3/2014
1

## Slide 2: #define hell in multi-platform embedded programming
2
© 2014 Schlumberger. All rights reserved.
An asterisk is used throughout this presentation to denote a mark of Schlumberger. Other company, product, and service names are the properties of their respective owners.
Notes: 4/3/2014
2

## Slide 3: Agenda
Our SW in perspective
#define hell
A better alternative
Summary

## Slide 4: Seismic
4
4/3/2014

## Slide 5: Seismic and Gun spread
Concentrator
200-400 m
8-14 streamers
8-12 km
Fiber
Concentrator
Sensors
Concentrator
6-8 Gun strings
Fiber
Concentrator
Guns

## Slide 6: Initial build system
UC8051
Coolflux DSP
Master
Slave
Master
Slave
Sensor Unit
Started with Master
Added Slave
Added Gun
Separate builds for each target
UC
DSP
PPC 405
Master
Slave
Gun
Master
Slave
Gun
Gun
Seismic
Back bone and
control

## Slide 7: Naming all combinations
Each unit (CS_SLAVE, CS_DGN, ….)
The Seismic units (CS_DSN)
The master unit (CS_MASTER)

## Slide 8: Code example
…
#if defined(CS_MASTER)
status->header.messageType = STAT_ERROR;
#elif defined(CS_SLAVE )
status->header.messageType = STAT_ERROR | DEST_CONS;
#endif // CS_SLAVE
…

## Slide 9: Code example
#if defined(CS_MASTER) && defined(CS_DSN)
#if defined(CS_MASTER)
#include <uC/Modules/Seismic/StatusMonitor.h>
#if defined(CS_DSN)
#include <uC/Drivers/Master/SbiDriverMaster.h>
#endif
#elif defined(CS_SLAVE)
#include <uC/Drivers/Common/Rtc.h>
#include <uC/Drivers/Slave/SbiDriverSlave.h>
#include <uC/Drivers/Common/SbiDriverCommon.h>
#include <uC/Drivers/Common/R8051XC_peripherals.h>
#endif // CS_SLAVE

## Slide 10: It gets ugly
switch(status->messageType) {
#if defined(CS_DSN)
#if defined(CS_MASTER)
case STAT_BOOTLOADER:
BSH_bootStatusReceived((DispArg_t) statusBuffer);
break;
case STAT_OVERDRIVE:
ODON_statusHandler((DispArg_t) statusBuffer);
break;
#endif // CS_MASTER
#elif defined(CS_DGN)
case STAT_FIRE_SOURCE:
SCTRL_setSourceTuning((DispArg_t) statusBuffer);
break;
#endif //CS_DGN
#if defined (CS_MASTER)
case STAT_NOMINAL_CFG:
NC_receiveSensorConfigError(statusBuffer);
break;
#endif
default:
CB_freeMem( (uint8_t XDATAMEM *) statusBuffer );
break;
}

## Slide 11: Initial build system
UC8051
Coolflux DSP
Master
Slave
Master
Slave
Sensor Unit
UC
DSP
PPC 405
Master
Slave
Gun
Master
Slave
Gun
Gun
Seismic
Back bone and
control

## Slide 12: Handling in the concentrator unit (Linux)
Same binary
NO if(boardType == CONS_PROTOTYPE_BOARD_REV_A)
Use a board info class
class BoardInfo
{
public:
uint32_t getNumSections ();
bool hasEthDevice();
bool hasPsuDevice();
int32_t getRtcDrifSpan();
double getEthRate(); }

## Slide 13: Board info class
uint32_t BoardInfo::getNumSections()
{
switch(m_boardType)
{
case CONS_EVALUATION_BOARD:
case CONS_BOARD:
return 1;
case CONS_PROTOTYPE_BOARD_REV_A:
return 2;
case CONS_PROTOTYPE_BOARD_REV_B:
case CONS_PROTOTYPE_BOARD_REV_C:
case X86_PLATFORM:
case CONS_V2_PROTOTYPE_BOARD_REV_A:
case CONS_V3_PROTOTYPE_BOARD_REV_A:
case CONS_V2_BOARD_REV_B:
return 4;
default:
throw StackException("Unknown board type");
}
}

## Slide 14: Build system after a few years
14
4/3/2014
UC
DSP
PPC 405
PPC 440
ARM Cortext M4
ARM
Cortext M3
Master
Slave
Gun
Master
Slave
Gun
Gun
Seismic
con1
con2
Main ctrl
con1
con2
Spare ctrl
Aux ctrl
con2
con2
Seismic Sensor
Back bone and
control
Power supply DSP
x86
Aux control

## Slide 15: Fresh start with Cortex targets
We want to do TDD
We wanted to avoid #define hell
We wanted to reuse common SW on 3 targets
Selected to use C++

## Slide 16: An I2C example
ARM
Cortext M3
SensorA
SensorB
Temperature
Reset count
I2C - 0
I2C - 2

## Slide 17: Dependency Injection
I2cSenATask
SenACH
SenA
I2cSenABus
Construct
Construct
Construct
main
Construct
I2cSenATask
SenACH
SenA
I2cSenABus
main
Construct

## Slide 18: Dependency Inversion
I2cSenATask
SenACH
SenA
I2cSenABus
I2cTask
I2cChipHandler
SenACH
SenBCH
TempCH
SenA
SenB
Temp
I2cBus
I2cBusConfig
ChipIrqHandler
ChipIrqConfig
I2cBusyWaitBus
High level modules should not depend upon low level modules. Both should depend upon abstractions.
Abstractions should not depend upon details. Details should depend upon abstractions.

## Slide 19: Dependency inserted code
SenAChip::SenAChip(I2cBus* i2cBus, OS *os, Logger* logger): m_i2cBus(i2cBus), m_os(os), m_logger(logger){}
uint8_t SenAChip::SetMode(SEN_A_Mode_t pm)
{
uint8_t value[2];
value[0] = SEN_A_CTRL_REG1;
if( !m_i2cBus->writeI2C(I2C_ADDRESS_SEN_A, 1, &value[0]) )
return 0;
if( !m_i2cBus->readI2C(I2C_ADDRESS_SEN_A, 1, &value[1]) )
return 0;
value[1] &= 0x1F;
value[1] |= (pm<<SEN_A_PM);
if( !m_i2cBus->writeI2C(I2C_ADDRESS_SEN_A, 2, &value[0]) )
return 0;
return 1;
}

## Slide 20: Dependency Inverted code
class I2cBus{
public:
I2cBus(){};
virtual ~I2cBus(){};
virtual uint8_t readI2C(uint8_t addr, unsigned int length, uint8_t* data) = 0;
virtual uint8_t writeI2C(uint8_t addr, unsigned int length, uint8_t* data) = 0;
};
class I2cBusBusyWait : public I2cBus{
public:
I2cBusBusyWait(uint32_t i2cBaseAddr, Logger* logger, OS* os);
virtual ~I2cBusBusyWait();
virtual uint8_t readI2C(uint8_t addr, unsigned int length, uint8_t* data);

## Slide 21: Tying it all together
void mainTask(void *unused)
{
OSFreeRTOS os;
MessageFactory MessageFactory(memChunk, NUMBER_OF_MESSAGES, &os, MESSAGE_ADDRESS_MAIN_CTRL);
I2cBusBusyWait i2cBusSenA(I2C0_MASTER_BASE, &logger, &os);
ChipIrqHandler sensAChipIrqHandler(GPIO_PORTF_BASE, GPIO_PIN_4, INT_GPIOF, sensAIntHandler, &os);
SenAChip sensAChip(&i2cBusSenA, &os, &logger);
SenAChipHandler sensAChipHandler(&i2cBusSenA, &sensAChip, &i2cRxQueue, &os, &logger);
I2cTask i2cSenATask("SenA", &os, &sensAChipIrqHandler, &logger);
i2cSenATask.addI2cChipHandler(&sensAChipHandler);
////// SenB
I2cBusBusyWait i2cBusSenB(I2C2_MASTER_BASE, &logger, &os);
ChipIrqHandler sensBChipIrqHandler(sensAIntHandler, &os);
SenBChip sensBChip(&i2cBusSenB, &os, &logger);
SenBChipHandler sensBChipHandler(&sensBChip, &i2cRxQueue, &os, &logger);
I2cTask i2cSenBTask("SenB", &os, &sensBChipIrqHandler, &logger);
i2cSenBTask.addI2cChipHandler(&sensBChipHandler);
main_main.cpp
main_aux.cpp
main_spare.cpp

## Slide 22: Adding some #define into paradise
#define CF_HAS_CANBUS
#define CF_HAS_SEN_A_AND_B
#define MY_CAN_INDEX 1
#define MESSAGE_ADDRESS_THIS_CTRL MESSAGE_ADDRESS_MAIN_CTRL
#define LED_SYSCTL_PERIPH_GPIO SYSCTL_PERIPH_GPIOK
#define I2C_BASE_SEN_A I2C0_MASTER_BASE
#define IRQ_PIN_SEN_A GPIO_PIN_4
#define IRQ_INTERUPT_SEN_A INT_GPIOF
#define I2C_BASE_SEN_B I2C2_MASTER_BASE
#include <main_common.h>
main_main.cpp
main_aux.cpp
main_spare.cpp
main_common.h

## Slide 23: main_common.h
void mainTask(void *unused)
{
uint8_t msgSource = MESSAGE_ADDRESS_THIS_CTRL;
OSFreeRTOS os;
MessageFactory MessageFactory(memChunk, NUMBER_OF_MESSAGES, &os, msgSource);
MessageQueue *uplinkQueue;
#ifdef CF_HAS_CANBUS
MessageQueue canbusTxQueue(&os, &MessageFactory, 20, 5000);
#endif
configureEmergencyBlink(LED_SYSCTL_PERIPH_GPIO, LED_GPIO_PORT_BASE, LED_GPIO_PIN);
#ifdef CF_MAIN
MessageQueue bnOutputQueue(&os, &MessageFactory, 20, 5000);
uplinkQueue = &bnOutputQueue;
#elif defined CF_SPARE
uplinkQueue = &canbusTxQueue;
#elif defined CF_AUX
uplinkQueue = &canbusTxQueue;
#endif

## Slide 24: More main_common.h
#ifdef CF_HAS_SEN_A_AND_B
I2cBusBusyWait i2cBusSenA(I2C_BASE_SEN_A, &logger, &os);
ChipIrqHandler sensAChipIrqHandler(IRQ_PORT_SEN_A, IRQ_PIN_SEN_A, IRQ_INT_SEN_A, sensAIntHandler, &os);
SenAChip sensAChip(&i2cBusSenA, &os, &logger);
SenAChipHandler sensAChipHandler(&i2cBusSenA, &sensAChip, &i2cRxQueue, &os, &logger);
I2cTask i2cSenATask("SenA", &os, &sensAChipIrqHandler, &logger);
i2cSenATask.addI2cChipHandler(&sensAChipHandler);
#ifdef CF_HAS_HUM_AND_RESET_SENSOR
HumTempChip humTempChip(&i2cBusSenA, &os, &logger);
HumTempChipHandler humTempChipHandler(&humTempChip, &i2cRxQueue, &os, &logger);
i2cSenATask.addI2cChipHandler(&humTempChipHandler);
#endif
I2cBusBusyWait i2cBusSenB(I2C_BASE_SEN_B, &logger, &os);
ChipIrqHandler sensBChipIrqHandler(sensAelIntHandler, &os);
SenBChip sensBChip(&i2cBusSenB, &os, &logger);
SenBChipHandler sensBChipHandler(&sensBChip, &i2cRxQueue, &os, &logger);
I2cTask i2cSenBTask("SenB", &os, &sensBChipIrqHandler, &logger);
i2cSenBTask.addI2cChipHandler(&sensBChipHandler);

## Slide 25: Summary
Make your HW dependent code relate to a real question
TDD helps a lot (also for C)
Avoid “just one little #define here since it is easy”
Build just one object per C/CPP file
Use a header file if you need different versions of a file
Extract out the difference to separate files
Structs are great for giving configurations
You don’t need to start out perfectly